## Slide 1: 3D Puzzle 3D printing algorithms course
Roy kinamon & alon mendelson

## Slide 2: Outline and Motivation
Motivation
  gain experience with 3D algorithms coding and hands on 3D printing
Outline
  Input: 3D body for print
  Output: Set of 3D printable puzzle pieces:
    Built into original shape
    Maintain stability and strength
  Efficient run time and easy printing

## Slide 3: Framework
3D representation and manipulation
  Trimesh
  Blender and OpenScad (for Boolean operations)
Printing
  MakerBot Replicator

## Slide 4: Algorithm stages – Slicing along Z
Optimize to keep cross section above minimal area
Keep continuity in xy plane
Represent slices with a Boolean grid of contained bolts and voids

## Slide 5: Algorithm stages – Plan X-Y Slicing
Recursive algorithm with greedy approach. runs on the Boolean representation with constraints:
  Pieces not too big and not to small
  Strong connection to adjacent layers
  No overlapping cuts between adjacent layers
Represent slicing as tree

## Slide 6: Algorithm stages – Add “Connectors” and slice
Add the bolts and the voids to each layer using Boolean operations
Perform slicing along x-y with recursive algorithm

## Slide 7: Print initial model with MakerBot replicator

## Slide 8: Bolts and voids Fine Tuning
First printed model was hard to assemble – pieces didn’t attach easily
Requires to adjust bolt and voids dimensions for ease of assembly but MakerBot resolution is low
We tried many different dimensions to find the best fit that:
  Maintains physical strength
  Pieces attaches and detaches easily
  “bridging” stays tensed

## Slide 9: Optimizing Structure strength
Measuring strength of single bolt over moment
Calculate total structure length and siameter
  Trial 1 – make it stand - aborted
    Filling
    Shape
  Trial 2
    Modifying bolt dimensions from friction to
    breaking pressure / flexural strength
Could not be completed due to makerbot print accuracy (different results per print)
hxy
dxy
P

## Slide 10: Optimizing Structure strength
Increase height and break resistance
  Infill (Higher infill for a stronger part)
  Shells (More shells for a stronger part)
  Print orientation, size or design
Increase diameter of bolts till meeting flexural strength

## Slide 11: Challenges
Trimesh and Blender are unstable
  Transition to OpenScad
Printing
  Alignment and Calibration
  Quality
  Duration - ~4 hours for layer
  “Debugging” is costly

## Slide 12: Thank You