## Slide 1: 3D Puzzle 3D printing algorithms course
Roy kinamon & alon mendelson

## Slide 2: Outline and Motivation
Motivation
  gain experience with 3D algorithms coding and hands on 3D printing
Outline
  Input: 3D body for print
  Output: Set of 3D printable puzzle pieces:
    Built into original shape
    Maintain stability and strength
  Efficient run time and easy printing

## Slide 3: Previous work in the field
Automated approaches for optimizing LEGO constructions (Primarily 2D)
Bricker - a blender extension converts any 3D Mesh into a photo-real 3D brick model
Chopper: Partitioning Models into 3D-Printable Parts

## Slide 4: Our work
Most of previous work is limited per our design target as most either
  Use Lego existing of shelf parts to build an approximate design target
  Minimal partitioning to fit printer size
As such we have developed all code and algorithms from scratch

## Slide 5: Framework
3D representation and manipulation
  Trimesh
  Blender and OpenScad (for Boolean operations)
Printing
  MakerBot Replicator
Technology Price
FDM ~2000$
Build volume
29.5 X 19.5 X 16.5 CM
Layer Resolution
100 micron

## Slide 6: Algorithm stages – Slicing along Z
We find a slicing that fulfills the following constraints:
  Slice height in some range
  cross section above minimal area (not too small)
  continuity in xy plane (slicing doesn’t separate model to parts)

## Slide 7: Algorithm stages – bolts and voids (בליטות וחורים)
We create a grid of bolts and voids within the model bounding box.
Grid is defined by bolts radius and distance between bolts
We represent the slices with a Boolean grid of contained bolts and voids.

## Slide 8: Algorithm stages – Plan X-Y Slicing
Recursive algorithm with greedy approach. runs on the Boolean representation with constraints:
  Pieces not too big and not to small
  Strong connection to adjacent layers
  No overlapping cuts between adjacent layers
Represent slicing as binary tree

## Slide 9: Algorithm stages – Add Bolts and Voids and slice
Add the bolts and the voids to each layer using Boolean operations
Perform slicing of the model along x-y with recursive algorithm operating on the binary tree

## Slide 10: Print initial model with MakerBot replicator

## Slide 11: Bolts and voids Fine Tuning
First printed model was hard to assemble – pieces didn’t attach easily
Requires to adjust bolt and voids dimensions for ease of assembly but MakerBot resolution is low
We tried many different dimensions to find the best fit that:
  Maintains physical strength
  Pieces attaches and detaches easily

## Slide 12: Optimizing Structure strength
Measuring strength of single bolt over moment
Calculate total structure length and siameter
  Trial 1 – make it stand - aborted
    Filling
    Shape
  Trial 2
    Modifying bolt dimensions from friction to
    breaking pressure / flexural strength
hxy
dxy
P

## Slide 13: Testing Bending moment
Optimizing Bolts and Voids Daimeter and height
Optimizing printer parmaeters per part:
  Layer height
  Infill density
  Infill Pattern
  No. of shells
  roof/Floor Thickness
For example at 0.1mm, 10%, Diamond, 2, 0.8mm ->
  Breaking point at 40N with 2.5cm result in:
  1Nm breaking moment

## Slide 14: Adjusting strength
In the case to the right
  F=0ex-ey+0ez, r= xex+0ey+0ez
We take COM in xy plane and calculate the Moment in –z axis
We check moment do not pass 1Nm per connecting dot
x
y

## Slide 15: Optimizing Structure strength
Increase height and break resistance
  Infill (Higher infill for a stronger part)
  Shells (More shells for a stronger part)
  Print orientation, size or design
Increase diameter of bolts till meeting flexural strength

## Slide 16: Results
Budha
Bunny
Print time (hours) | Algo runtime (mins) | No. pieces | Bounding Box (cm) | 
~11 | ~3 | 12 | 10X5X12 | Budha
~17 | ~7 | 23 | 10X6X13 | Bunny

## Slide 17: Challenges
Trimesh and Blender are unstable
  Transition to OpenScad
Printing
  Alignment and Calibration
  Quality
  Duration
  “Debugging” is costly

## Slide 18: Thank You